## Slide 1
SPI Master (Mode-0) Implementation
A synchronous serial communication protocol implementation for embedded systems, developed by student team
2023-EE-173 2023-EE-181
2023-EE-185 2023-EE-167.

## Slide 2
Introduction to SPI
Serial Peripheral Interface
A synchronous serial communication protocol for embedded systems.
Historical Context
Developed by Motorola in the mid-1980s.
Wide Application
Widely used in modern embedded systems for device communication.

## Slide 3
Literature Review
1
Design and Implementation of SPI Master Slave Using Verilog HDL
IEEE Conference, 2019. Focused on efficient state machine design and resource optimization.
2
FPGA-Based Implementation of SPI Communication Protocol
International Journal, 2020. Emphasized timing optimization and FPGA-specific considerations.
3
High-Speed SPI Master Controller Design
IEEE Transactions on VLSI Systems. Featured multiple slave support and clock management techniques.

## Slide 4
Why SPI?
Simple Hardware Implementation
Full-duplex communication
No complex addressing
Minimal pin requirements
Wide Industry Support
Sensors and memory devices
Display controllers
ADCs/DACs

## Slide 5
Project Specifications
Hardware Target
Xilinx Artix-7 FPGA
SystemVerilog implementation
8-bit data width
Mode-0 operation
Clock Specifications
System clock: 100 MHz
SPI clock: 25 MHz
Configurable division ratio

## Slide 6
Interface Specifications
Input Signals
clk (System clock)
rst_n (Active-low reset)
start (Start transmission)
data_in (8-bit data)
Output Signals
mosi (Master Out Slave In)
sclk (Serial Clock)
cs_n (Chip Select)
busy/done (Status signals)

## Slide 7
Timing Specifications
Clock Characteristics
CPOL = 0 (Clock idles low)
CPHA = 0 (Sample on rising edge)
Setup Time
2ns minimum before clock edge
Hold Time
1ns minimum after clock edge
Clock to Output
5ns maximum delay

## Slide 8
Design Architecture
Control Logic
State machine and timing control
Data Path
Shift register and bit counter
Interface
Signal drivers and receivers
The SPI Master connects data_in, start, clk, and rst_n inputs to mosi, sclk, cs_n, busy, and done outputs through a structured architecture.

## Slide 9
State Machine
IDLE
Wait for start signal
LOAD
Load data into shift register
TRANSFER
Send bits serially
COMPLETE
Signal done and return to IDLE

## Slide 10
Verification Plan
Test Cases
Basic data transfer
Reset during transfer
Back-to-back transfers
Error conditions
Coverage Goals
100% state coverage
100% transition coverage
Signal toggle coverage
Verification Environment
SystemVerilog testbench
Self-checking assertions
Automated regression tests